## Slide 1: How to use dfu-util for Ameba Pro2

## Slide 2: Install the libusb driver
1.Plug the Ameba Pro to PC and open Zadig
2.Select the USB DFU CLASS
3.Select the libusb-win32
4.Install driver

## Slide 3: Install the libusb driver -cont
Check whether the driver is installed
Open the device manager
We can see the USB DFU CLASS

## Slide 4: Update the FW from DFU
Burn the DFU firmware to Ameba Pro.
Execute the below command
  dfu-util.exe -d 1d6b:0202 -a 0 -D ota.bin

## Slide 5: Note
It only support win7 and win10 64bit operation system for libusb driver.